## Slide 1
Launch Application
Select HDLGen File
Set SoC Builder Configuration (I/O, Vivado Settings)
Vivado will execute all build steps required
Find output files in
<hdlgen-proj>/PYNQBuild/output
Upload all files in output/ to PYNQ
Vivado is launched from the terminal using Python
(Python opens a shell session, it opens Vivado by calling vivado.bat in the installation directory)
Vivado sources (executes) a Tcl (Tool control language) script with the build instructions which was prepared by the SoC builder in the previous step.
Click “Run” in SoC Builder to start build
SoC Builder creates a script with all instructions and Vivado executes the build instructions to produce binary files.
Upon a successful build, SoC builder finds the bitstream output and dependencies and moves them to PYNQBuild/output directory
Remote: Open remote Jupyter Notebook environment in your browser, select the upload button and select all files in PYNQBuild/output
Local (LAN or Direct Connection): You may upload files manually or choose to upload automatically, supplying IP address of the PYNQ board.
Using information read from the XML, instructions are generated in Tcl language to execute the following steps:
Launch Vivado
(Optional) Make the Vivado GUI visible
Change target board configuration to PYNQ Z2
Import FPGA’s Physical Constraints
Create and populate a block design connecting PYNQ Processing System to the VHDL Logic Component by AXI IP.
Run Synthesis
Run Implementation
Generate and Export Bitstream
Export Block Diagram
An XDC Master Physical Constraints File is also generated automatically depending on the I/O configuration specified by the user in the GUI. The XDC file maps board I/O to external ports in the block diagram.
Using information read from the XML, instructions are generated in Tcl language to execute the following steps:
Launch Vivado
(Optional) Make the Vivado GUI visible
Set target board configuration to PYNQ Z-2
  If the board config does not exist in the user’s installation of Vivado, install it automatically.
Import FPGA’s Physical Constraints
  Physical constraints are generated depending on I/O config. This file maps external pins in block design to board I/O pins.
Create and populate a block design connecting PYNQ Processing System to the VHDL Logic Component by AXI IP.
  Import Component
  (Optional) An SVG image of component may be exported at this point. It will be used later and presented in the Jupyter Notebook fiel
  Import Zynq Processing Unit
  For each signal in the component:
    Import AXI GPIO Component
    Configure AXI GPIO
    Connect user component port to GPIO
  Import AXI Interconnect IP
  Connect each AXI GPIO to the Interconnect IP
  Import System Reset IP
  Connect System Reset to the Interconnect IP
  Run Connection Automation on Block Design
  Run Block Automation on Block Design
  Auto assign memory addresses
  Validate Block Design
A HDL Wrapper is generated automatically by Vivado
Run Synthesis
Run Implementation
Generate and Export Bitstream
Export Block Diagram
(Optional) The user may set Vivado not to close automatically allowing them inspect the project for their own purposes.
Close project, close GUI and exit Vivado
Whilst Vivado is executing the steps, the SoC builder will run multiple threads used to track the main application log, the synthesis log and the implementation log files.
The SoC Builder checks continuously to determine what stage in the build process Vivado is in, and relay this to the user through the GUI. The logs will also inform the SoC builder if there is any errors or critical warnings, handling errors and relaying info to user.
Find output files in
<hdlgen-proj>/PYNQBuild/output
Upon a successful build, SoC builder finds the bitstream output and dependencies and moves them to PYNQBuild/output directory
SoC Builder reads all the required information from the HDLGen Project XML file

## Slide 2
Launch Application
Select HDLGen File
Set SoC Builder Configuration (I/O, Vivado Settings)
Vivado will execute all build steps required
Find output files in
<hdlgen-proj>/PYNQBuild/output
Upload all files in output/ to PYNQ
Vivado is launched from the terminal using Python
(Python opens a shell session, it opens Vivado by calling vivado.bat in the installation directory)
Vivado sources (executes) a Tcl (Tool control language) script with the build instructions which was prepared by the SoC builder in the previous step.
Click “Run” in SoC Builder to start build
SoC Builder creates a script with all instructions and Vivado executes the build instructions to produce binary files.
Upon a successful build, SoC builder finds the bitstream output and dependencies and moves them to PYNQBuild/output directory
Remote: Open remote Jupyter Notebook environment in your browser, select the upload button and select all files in PYNQBuild/output
Local (LAN or Direct Connection): You may upload files manually or choose to upload automatically, supplying IP address of the PYNQ board.
Using information read from the XML, instructions are generated in Tcl language to execute the following steps:
Launch Vivado
(Optional) Make the Vivado GUI visible
Change target board configuration to PYNQ Z2
Import FPGA’s Physical Constraints
Create and populate a block design connecting PYNQ Processing System to the VHDL Logic Component by AXI IP.
Run Synthesis
Run Implementation
Generate and Export Bitstream
Export Block Diagram
An XDC Master Physical Constraints File is also generated automatically depending on the I/O configuration specified by the user in the GUI. The XDC file maps board I/O to external ports in the block diagram.
Using information read from the XML, instructions are generated in Tcl language to execute the following steps:
Launch Vivado
(Optional) Make the Vivado GUI visible
Set target board configuration to PYNQ Z-2
  If the board config does not exist in the user’s installation of Vivado, install it automatically.
Import FPGA’s Physical Constraints
  Physical constraints are generated depending on I/O config. This file maps external pins in block design to board I/O pins.
Create and populate a block design connecting PYNQ Processing System to the VHDL Logic Component by AXI IP.
  Import Component
  (Optional) An SVG image of component may be exported at this point. It will be used later and presented in the Jupyter Notebook fiel
  Import Zynq Processing Unit
  For each signal in the component:
    Import AXI GPIO Component
    Configure AXI GPIO
    Connect user component port to GPIO
  Import AXI Interconnect IP
  Connect each AXI GPIO to the Interconnect IP
  Import System Reset IP
  Connect System Reset to the Interconnect IP
  Run Connection Automation on Block Design
  Run Block Automation on Block Design
  Auto assign memory addresses
  Validate Block Design
A HDL Wrapper is generated automatically by Vivado
Run Synthesis
Run Implementation
Generate and Export Bitstream
Export Block Diagram
(Optional) The user may set Vivado not to close automatically allowing them inspect the project for their own purposes.
Close project, close GUI and exit Vivado
Whilst Vivado is executing the steps, the SoC builder will run multiple threads used to track the main application log, the synthesis log and the implementation log files.
The SoC Builder checks continuously to determine what stage in the build process Vivado is in, and relay this to the user through the GUI. The logs will also inform the SoC builder if there is any errors or critical warnings, handling errors and relaying info to user.
Find output files in
<hdlgen-proj>/PYNQBuild/output
Upon a successful build, SoC builder finds the bitstream output and dependencies and moves them to PYNQBuild/output directory
SoC Builder reads all the required information from the HDLGen Project XML file

## Slide 3
Connection between Computer and Router can be Ethernet or Wi-Fi
Router is connected to PYNQ Z-2 board by Ethernet connection
User uploads binaries to the PYNQ Z2 over the LAN connection
PYNQ (Unix-based) OS and user-uploaded files are stored in on-board MicroSD
Zynq 7000 SoC consisting of a dual-core ARM processor and 13,300 logic slice programmable logic
PYNQ hosts a Jupyter Notebook session in web interface accessible in the computer’s web browser
PYNQ (Unix-based) OS and user-uploaded files are stored in on-board MicroSD
Zynq 7000 SoC consisting of a dual-core ARM processor and 13,300 logic slice programmable logic
Computer directly connected to FPGA using Ethernet connection
PYNQ hosts a Jupyter Notebook session in web interface accessible in the computer’s web browser
Bitstream files are used to program the PL (programmable logic) slices in the FPGA core
Bitstream files are used to program the PL (programmable logic) slices in the FPGA core
PYNQ (Unix-based) OS and user-uploaded files are stored in on-board MicroSD
Zynq 7000 SoC consisting of a dual-core ARM processor and 13,300 logic slice programmable logic
Computer directly connected to FPGA using Ethernet connection
PYNQ hosts a Jupyter Notebook session in web interface accessible in the computer’s web browser
Bitstream files are used to program the PL (programmable logic) slices in the FPGA core