## Slide 1
dIn1
dIn0
dOut
Mux2_1 Walkthrough
sel
dIn0 | dIn1 | sel | dOut
X | Y | 0 | X
X | Y | 1 | Y
Truth Table
dIn0 | dIn1 | sel | dOut
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
Test Plan
Component Symbol
Target Language: Verilog

## Slide 2
addIn1
dOut
2-bit Full Adder Walkthrough
Truth Table & Test plan
Component Symbol
Target Language: VHDL
addIn0
cOut
addIn1 | addIn0 | cIn | dOut | cOut
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
cIn

## Slide 3
RISC-V ALU Walkthrough
Component Symbol
Target Language: VHDL
A
B
ALUOut
selALUOp
branch
32
32
32

## Slide 4
RISC-V ALU Walkthrough
Test plan
Signals | selALUOp | A | B | ALUOut | branch | Delay | TestNo | Note
Mode | in | in | in | out | out | None | None | None
Radix | 4'b | 32'h | 32'h | 32'h | 1'b | None | None | None
= | = | = | = | = | = | = | = | =
 | 0000 | 5a5a5a5a | 15a5a5a6 | 70000000 | 0 | 1 | 1 | sgnA + sgnB
 | 0000 | 15a5a5a6 | 5a5a5a5a | 70000000 | 0 | 1 | 2 | sgnA + sgnB
 | 0000 | ffffffff | 40000000 | 3fffffff | 0 | 1 | 3 | 
 | 0001 | ffffffff | fffffffe | 00000001 | 0 | 1 | 4 | sgnA - sgnB
 | 0010 | f0c3a596 | 1f7e8ab4 | 10428094 | 0 | 1 | 5 | A and B
 | 0011 | f0c3a596 | 1f7e8ab4 | ffffafb6 | 0 | 1 | 6 | A or B
 | 0100 | f0c3a596 | 1f7e8ab4 | efbd2f22 | 0 | 1 | 7 | A xor B
 | 0101 | f0c3a596 | 00000008 | c3a59600 | 0 | 1 | 8 | A << B(4:0) shift left logical
 | 0110 | f0c3a596 | 00000008 | 00f0c3a5 | 0 | 1 | 9 | A >> B(4:0) shift right logical
 | 0111 | f0c3a596 | 00000008 | fff0c3a5 | 0 | 1 | 10 | A >>> B(4:0) shift right arithmetic
 | 1000 | f0c3a596 | 1f7e8ab4 | 00000001 | 0 | 1 | 11 | 1 if sgn A < sgn B
 | 1001 | f0c3a596 | 1f7e8ab4 | 00000000 | 0 | 1 | 12 | 1 if uns A < uns B
 | 1010 | f0c3a596 | 1f7e8ab4 | 00000001 | 0 | 1 | 13 | branch = 1 if A = B
 | 1010 | f0c3a596 | f0c3a596 | 00000002 | 1 | 1 | 14 | branch = 1 if A = B
 | 1011 | f0c3a596 | 1f7e8ab4 | 00000003 | 1 | 1 | 15 | branch = 1 if A != B
 | 1011 | f0c3a596 | f0c3a596 | 00000004 | 0 | 1 | 16 | 
 | 1100 | f0c3a596 | 1f7e8ab4 | 00000005 | 1 | 1 | 17 | branch = 1 if sgn A < sgnB
 | 1100 | f0c3a596 | f0c3a596 | 00000006 | 0 | 1 | 18 | 
 | 1101 | f0c3a596 | 1f7e8ab4 | 00000007 | 0 | 1 | 19 | branch = 1 if sgn A >= sgnB
 | 1101 | f0c3a596 | f0c3a596 | 00000008 | 1 | 1 | 20 | 
 | 1110 | f0c3a596 | 1f7e8ab4 | 00000009 | 0 | 1 | 21 | branch = 1 if uns A < uns B
 | 1110 | f0c3a593 | f0c3a596 | 00000010 | 1 | 1 | 22 | 
 | 1111 | f0c3a596 | 1f7e8ab4 | 00000011 | 1 | 1 | 23 | branch = 1 if uns A >= uns B
 | 1111 | f0c3a596 | f0c3a596 | 00000012 | 1 | 1 | 24 | 

## Slide 5
dataIn(3:0)
count(3:0)
CB4CLED Walkthrough
Component Symbol
Target Language: VHDL
load
4-bit Cascadable, Chip-Enabled, Up/Down Synchronous Counter
with Asynchronous reset
up
ce
clk
rst
ceo
TC

## Slide 6
CB4CLED Walkthrough
4-bit Cascadable, Chip-Enabled, Up/Down Synchronous Counter
with Asynchronous reset

## Slide 7
sw
aShot
Single Shot Walkthrough
Timing Diagram
Component Symbol
Target Language: VHDL
clk
rst